## Slide 1: Comparison and merging of ozone profile data from lidar and other measurement techniques
S. Godin-Beekmann1, S. Khaykin1, M. Pastel1, K. Hocke2, E. Mahieu3, M. Palme4
1LATMOS, UVSQ-CNRS, France
2U. Bern, Switzerland
3U. Liège, Belgium
4U. Bremen, Germany
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 2: Background
NDACC: Implementation of several instrumental techniques for the long-term measurement of ozone vertical distribution, e.g. lidar, microwave and FTIR spectrometers
MACC – Monitoring Air Composition and Climate parameters: European project for the analysis and forecast of atmospheric composition & related parameters at global and regional scale (Copernicus programme)
Use of NDACC data to validate MACC ozone products (NORS European project)
La Réunion
Izaña
Ny Alesund
Alpine stations
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 3: Rationale of the study
Within NDACC, the variety of ozone profile measuring techniques provide measurements with different altitude range, vertical resolution, uncertainty, etc...
Example of ozone profile measurements at NyAlesund
sonde
lidar
MW
MW
sonde
FTIR
Objectives
Develop a methodology for combining the various data sets and provide consistent ozone vertical distribution time series for MACC ozone fields validation
Provide easy to use ozone data series for end users
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 4
Ozone Measurements at OHP
Haute-Provence Observatory:
44°N, 6°E – part of NDACC
Various lidar measurements since late 70s and 80s: temperature, ozone, wind, aerosols, water vapor
Total ozone measurements:
  Dobson spectrometer since September 1983
  SAOZ UV-Visible spectrometer since January 1992
Ozone vertical distribution
  Stratospheric ozone lidar (1985 – routine from 1986)
  Tropospheric ozone lidar since 1991
  Ozone sondes: ECC from 1991 (SPC up to 1997, ENSCI)
  Dobson Umkehr since 1983
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 5: Measurement techniques
DIfferential Absorption Lidar technique
Active technique
Emission of two laser radiations at wavelengths characterized by a different ozone absorption cross section (308 nm and 355 nm)
MicroWave Ozone spectrometer
Fourier Transform InfraRed spectrometer
Passive technique
Measures ozone emission lines in the submillimeter range
Passive technique
Atmospheric absorption spectra used for the retrieval of ozone
wide spectral range 600 – 4500 cm−1
high spectral resolution
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 6: Vertical resolution
 | Altitude range (km) | Resolution (km)
LIDAR | 10 – 45 | 1 – 4.5
Microwave | 20 – 60 | 10 – 15
FTIR | 4 – 42 | 7 – 15
Ozone sondes | 0 – 35 | 0.3
OHP lidar
Microwave Bern
FTIR Jungfraujoch
Active remote sensing
Passive remote sensing

## Slide 7: Evaluation of systematic differences
Example of Alpine station climatological differences
A priori profile correction
MW: monthly climatology
FTIR: annual climatology
-> correction of FTIR a priori
FTIR - MW
FTIR corr - MW
MW - DIAL smoothed
DIAL – ECC sondes
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 8: Systematic differences with AURA-MLS
Annual average
MW - MLS smoothed
DIAL – MLS
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 9: Ozone profile integration
Ny Alesund
Alpine station
Main steps:
Smooth higher resolved profiles using AVK (FTIR, MW)
Check for difference in a priori
Check for systematic bias (MLS)
Data integration
Error weight
Instrumental bias
Geophysical bias
Merged ozone profile reported for more than one measurement at the station
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 10: Geophysical bias
Difference between coincident MLS ozone measurements at OHP and Jungfraujoch
Equivalent latitude difference between OHP and Bern (°) - 2013
Ozone mixing ratio vs equivalent latitude
500 K
650 K
Very small geophysical bias between the stations
Distance between stations:
Bern – Jungfraujoch: ~ 60 km
OHP – both other stations: ~ 400 km
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 11: Alpine station
Merged ozone profile data: nb of meas.
Smoothed OHP lidar data (Bern MW averaging kernels) 1299
Bern MW data corrected from climatological bias with MLS 3798
Jungfraujoch FTIR data corrected using MW a priori profiles 1169
Smoothed OHP ozone sonde data (Jungfraujoch FTIR averaging kernels) 448
Smoothed Payerne ozone sonde data (Jungfraujoch FTIR averaging kernels) 1521
Coincidences:
1389 more than 2 meas.
869 more than 3 meas.
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 12: Alpine station
merged O3 vs individual
merged O3 vs MLS
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba
35 – 40 km
25 – 30 km
15 – 20 km

## Slide 13: Alpine station
Ozone partial columns
Comparison of total ozone columns with SAOZ measurements
Calculation of tropopause altitude using NCEP data
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 14: NyAlesund (Norway)
Merged ozone profile data: nb of meas.
Smoothed lidar data (MW averaging kernels) 129
MW data corrected from bias with MLS data 1216
FTIR data 83
Smoothed ozone sonde data (FTIR averaging kernels) 811
Coincidences:
310 more than 2 meas.
17 More than 3 meas.
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 15: Ny Alesund
merged O3 vs individual
merged O3 vs MLS
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba
15 – 20 km
25 – 30 km
35 – 40 km

## Slide 16: Izaña and La Réunion Island
Only FTIR and ozone sondes measurements at both stations
few ozone lidar measurements at La Réunion Island over the period
Izaña
362 coincidences
La Réunion
48 coincidences
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 17: Conclusions
Long-term ozone profile time series characterized by different vertical resolution and altitude ranges are available since the early nineties at NDACC stations.
Combined ozone profile data sets have been produced at 4 NDACC stations together with stratospheric and tropospheric partial columns
Good consistency of the data products with satellite measurements and good comparison with total ozone measurements (SAOZ)
Data delivered within the European NORS project and available for use upon request
Next step: detailed comparison with MACC ozone products
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba

## Slide 18: Thank you for your attention!
VIII WLMLA , 6 – 10 April 2015, Cayo Coco, Cuba